TECHNICAL BULLETIN

Date:  14th Apr 04  (rev 23 Aug 05) rev 5					No:  96

Raised by: T C

Distributed to: As required

Soundtracs Digico,  unit 10 Silverglade Business Park Chessington Surrey KT9 2QL  England

Tel: +44 (0)1372 845600  Fax: +44 (0)1372 845656  email: support@digiconsoles.com

_____________________________________________________________________________

COMBINED GENERAL PURPOSE INPUT/OUTPUT + MIDI OPTION   (GPIO CARD)

FITTING & hardware CONNECTIONS TO P15081 PCB

Fitting the GPIO option to Digico & Soundtracs digital mixers involves adding 1 small interface PCB and connecting this to a control line and power supply.

WARNING: These  Worksurfaces contain dangerous voltages: AC mains , DC at very high voltage & high frequency high voltage backlight supplies. Disconnect the mains supply cable(s) to the mixer before attempting any internal work! The following fitment should be carried out by qualified personnel only!

FITTING IN D4, D5, DS00,

The GPIO PCB is fitted directly to the rear panel of the mixer by its 37way D connector using M3 nuts and bolts supplied.  The cutout is normally covered by a blanking label, which must first be removed.

This part of the rear panel is accessible by lifting the upper input control panel to the left of the upper master section from the mixer frame. This held in with hex socket screws. Use the hex driver supplied with the mixer. This panel need not be disconnected but can be propped up to allow access underneath. The  Main PSU is under the master section. The panel should be lifted in the same way as the input section if required for access to power.

FITTING IN D5, D5T AND ALL + RE versions

The GPIO PCB is fitted directly to the rear panel of the mixer by its 37way D connector using M3 nuts and bolts supplied.  The cutout is covered by a blanking label, which must first be removed.

Withdraw the DSP engine drawer, release 4 retaining screws.  Remove the drawer lid to gain access to rear panel.

FITTING IN DS3 or DPC

DS3 and DPC software does not support this GPIO and separate GPO and GPI cards must be used. Refer to TN 76 and 101 for details

INTERNAL CONNECTIONS

The PCB has 2 connectors, power and control.  Looms are provided in the kit to connect these within the mixer.

The 4 pin female power connector fits to CN3 on the PCB.  The “piggy back” power  take off connection goes in line with either of the matching power connections on the distribution PCB on the rear of the main PSU or to the free power loom connector tied back inside the mixer. Be sure to reconnect the existing plug in line.

TB 96                 page 2

A 10 way ribbon control connection loom is provided. This connects to CN2 on the GPIO PCB. The other end connects to the “time code” PCB P13875.  This is an ISA card on the PC motherboard. It has several 10 way ribbon cables already fitted (the number depends on how many worksurface panels are fitted to the mixer).

The control cable goes to the next free socket counting away from the PC mounting panel. Note if there is an odd number of ribbons already fitted the new cable, goes in the socket under the last occupied socket. refer to drawing below. Note the DS00 and some other mixers may already be equipped with 10 way looms preinstalled but not connected.

Ensure cable as installed are routed so as to allow free removal of other PCBs in the DSP system. In particular, do not route cables across the top of the DSP system.

Tie back cables with small Tywraps to prevent cables snagging or rubbing on other components, sharp edges etc.

EXTERNAL CONNECTIONS

This card replaces the 2 individual 16 way input and output options (GPI and GPO or “fader start”).

It combines 16 GPI and 16 GPO with 1 MIDI in-out-thru port in addition to the midi port already provided on the mixer.

The connections are on a single high density series D connector, with 62 pins (this uses a standard 37 Way D sized shell)

Two tables follow arranged by pin number and function.

Connection Notes

GPO Relay outputs are SPST make connects. These are floating on connections A and B.

Contact are rated 0.5A  100V dc (max 10W)

GPI inputs are logic (non isolated) requiring a make to 0V (earth). These have internal pull-up 22K to +5V. A simple single pole switch or relay (make to 0V) will trigger the input.

The +5V present is fused internally for logic level use only.

MIDI connections are to published midi standards.

TB 96                 page 3

Programming

See separate notes relevant to the mixer model in use for programming information. GPO’s are programmed in the sockets file, GPI’s in a separate script file declared in the hardware configuration and written separately.

If the card is not declared in the hardware configuration, a worksurface error will result. This is normal the first time the system is operated with the new card in place, until the system configuration is amended to include this card.

Note that declarations referring to GPI and GPO ports are set equal for a combi card which the system will then recognise as such. There are no separate declarations for a combi card.

e.g

GPI port = 5

GPO port = 5

When using the digiconfig hardware edit details program, the GPI and GPO will default to different ports, and must be manually changed to be equal (on the port used to connect the hardware.

Note that a GPI script file should be declared in the configuration page. If this is not yet present, a “file not found” error message will appear until it is written.

TB 96                 GPIO connections   2 pages

NOTE:  GPI and GPO column list equivalent conversion/connection to older type P14639 GPO and GPI PCB’s

|  | Sorted by pin |  |  |  |  | Sorted by function |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Pin | Function | Note | GPO | GPI |  | Function | Pin | Note | GPO | GPI |
| 1 | GPO 13A |  |  | 28 |  | +5V | 49 |  |  |  |
| 2 | GPO 12A |  |  | 26 |  | +5V | 50 |  |  |  |
| 3 | GPO 11A |  |  | 24 |  | 0V | 51 |  |  | COM* |
| 4 | GPO 10A |  |  | 22 |  | 0V | 52 |  |  |  |
| 5 | GPO 09A |  |  | 20 |  | 0V | 53 |  |  |  |
| 6 | GPO 08A |  |  | 16 |  | 0V | 54 |  |  |  |
| 7 | GPO 07A |  |  | 14 |  | 0V | 55 | Midi (out) | DIN | 2 |
| 8 | GPO 06A |  |  | 12 |  | 0V | 58 | Midi (thru) | DIN | 2 |
| 9 | GPO 05A |  |  | 10 |  | GPI 01 | 21 |  | 3 |  |
| 10 | GPO 04A |  |  | 8 |  | GPI 02 | 42 |  | 42 |  |
| 11 | GPO 03A |  |  | 6 |  | GPI 03 | 20 |  | 7 |  |
| 12 | GPO 02A |  |  | 4 |  | GPI 04 | 41 |  | 41 |  |
| 13 | GPO 01A |  |  | 2 |  | GPI 05 | 19 |  | 11 |  |
| 14 | GPI 15 |  | 33 |  |  | GPI 06 | 40 |  | 13 |  |
| 15 | GPI 13 |  | 29 |  |  | GPI 07 | 18 |  | 15 |  |
| 16 | GPI 11 |  | 25 |  |  | GPI 08 | 39 |  | 17 |  |
| 17 | GPI 09 |  | 21 |  |  | GPI 09 | 17 |  | 21 |  |
| 18 | GPI 07 |  | 15 |  |  | GPI 10 | 38 |  | 23 |  |
| 19 | GPI 05 |  | 11 |  |  | GPI 11 | 16 |  | 25 |  |
| 20 | GPI 03 |  | 7 |  |  | GPI 12 | 37 |  | 27 |  |
| 21 | GPI 01 |  | 3 |  |  | GPI 13 | 15 |  | 29 |  |
| 22 | GPO 13B |  |  | 29 |  | GPI 14 | 36 |  | 29 |  |
| 23 | GPO 12B |  |  | 27 |  | GPI 15 | 14 |  | 33 |  |
| 24 | GPO 11B |  |  | 25 |  | GPI 16 | 35 |  | 35 |  |
| 25 | GPO 10B |  |  | 23 |  | GPO 01A | 13 |  |  | 2 |
| 26 | GPO 09B |  |  | 21 |  | GPO 01B | 34 |  |  | 3 |
| 27 | GPO 08B |  |  | 17 |  | GPO 02A | 12 |  |  | 4 |
| 28 | GPO 07B |  |  | 15 |  | GPO 02B | 33 |  |  | 5 |
| 29 | GPO 06B |  |  | 13 |  | GPO 03A | 11 |  |  | 6 |
| 30 | GPO 05B |  |  | 11 |  | GPO 03B | 32 |  |  | 7 |
| 31 | GPO 04B |  |  | 9 |  | GPO 04A | 10 |  |  | 8 |
| 32 | GPO 03B |  |  | 7 |  | GPO 04B | 31 |  |  | 9 |
| 33 | GPO 02B |  |  | 5 |  | GPO 05A | 9 |  |  | 10 |
| 34 | GPO 01B |  |  | 3 |  | GPO 05B | 30 |  |  | 11 |
| 35 | GPI 16 |  | 35 |  |  | GPO 06A | 8 |  |  | 12 |
| 36 | GPI 14 |  | 29 |  |  | GPO 06B | 29 |  |  | 13 |
| 37 | GPI 12 |  | 27 |  |  | GPO 07A | 7 |  |  | 14 |
| 38 | GPI 10 |  | 23 |  |  | GPO 07B | 28 |  |  | 15 |
| 39 | GPI 08 |  | 17 |  |  | GPO 08A | 6 |  |  | 16 |
| 40 | GPI 06 |  | 13 |  |  | GPO 08B | 27 |  |  | 17 |
| 41 | GPI 04 |  | 41 |  |  | GPO 09A | 5 |  |  | 20 |
| 42 | GPI 02 |  | 42 |  |  | GPO 09B | 26 |  |  | 21 |
| 43 | GPO 14A |  |  | 30 |  | GPO 10A | 4 |  |  | 22 |
| 44 | GPO 14B |  |  | 31 |  | GPO 10B | 25 |  |  | 23 |
| 45 | GPO A15 |  |  | 32 |  | GPO 11A | 3 |  |  | 24 |
| 46 | GPO B15 |  |  | 33 |  | GPO 11B | 24 |  |  | 25 |
| 47 | GPO 16A |  |  | 34 |  | GPO 12A | 2 |  |  | 26 |
| 48 | GPO 16B |  |  | 35 |  | GPO 12B | 23 |  |  | 27 |
| 49 | +5V |  |  |  |  | GPO 13A | 1 |  |  | 28 |
| 50 | +5V |  |  |  |  | GPO 13B | 22 |  |  | 29 |
| 51 | 0V |  | DIN |  |  | GPO 14A | 43 |  |  | 30 |
| 52 | 0V |  |  |  |  | GPO 14B | 44 |  |  | 31 |
| 53 | 0V |  |  |  |  | GPO 16A | 47 |  |  | 34 |
| 54 | 0V |  |  |  |  | GPO 16B | 48 |  |  | 35 |
| 55 | 0V | Midi (out) | DIN | 2 |  | GPO A15 | 45 |  |  | 32 |
| 56 | MIDI OUT- |  | DIN | 5 |  | GPO B15 | 46 |  |  | 33 |
| 57 | MIDI OUT+ |  | DIN | 4 |  | MIDI IN- | 61 |  | DIN | 5 |
| 58 | 0V | Midi (thru) | DIN | 2 |  | MIDI IN+ | 62 |  | DIN | 4 |
| 59 | MIDI THRU- |  | DIN | 5 |  | MIDI OUT- | 56 |  | DIN | 5 |
| 60 | MIDI THRU+ |  | DIN | 4 |  | MIDI OUT+ | 57 |  | DIN | 4 |
| 61 | MIDI IN- |  | DIN | 5 |  | MIDI THRU- | 59 |  | DIN | 5 |
| 62 | MIDI IN+ |  | DIN | 4 |  | MIDI THRU+ | 60 |  | DIN | 4 |

*  GPI inputs common is 0V.

This can also be connected to even numbered pins 2,4,6 etc. to pin 34 on the GPI card (but NOT Combi PCB)

DIN numbers refer to Midi DIN connectors,

3 external sockets required, IN OUT & THRU, only 2 are earthed by pin 2